## Slide 1
3
Bab
Keselamatan Konstruksi dan Permesinan
Disusun oleh Tim Dosen K3L FTUI
Genap 2019/2020

## Slide 2: Pengantar
1-1
Risiko dalam suatu kegiatan konstruksi atau industrial perlu dikaji dalam sistem manajemen kesehatan dan keselamatan kerja untuk setiap tahapan dalam siklus hidup suatu proyek, plant atau teknologi.
[Hammurabi]
Referensi: dari berbagai sumber.

## Slide 3: Keselamatan Konstruksi
  Designing for Construction Safety is the process of of addressing construction site safety and maintenance in the design phase of a project.
  The customary role of the design professional is protect the safety of the public and to comply with building codes.
  Designing for Construction Safety extends this role to include construction site safety.

## Slide 4: 1. Recognized Hazards
Gravity-Falls from elevation
Falling objects
Slopes-Upset
Rollover
Unstable surfaces
Water- Drowning

## Slide 5: Recognized Hazards
Walking/working surfaces-
tripping, slipping
Mechanical hazards-
Rotation, reciprocation, shearing,
vibration, pinch points, hydraulics,
pneumatics, entanglement

## Slide 6: Recognized Hazards
Stored energy- springs, pneumatics
hydraulics, capacitors
Electrical-electrostatic, current, voltage, sparks, arcs
Chemical-corrosive, combustion, toxic

## Slide 7: Recognized Hazards
Biological-allergens, carcinogens
Radiant Energy-sound, nuclear,
X-rays, light, lasers

## Slide 8
Keselamatan dalam evolusi proyek konstruksi

## Slide 10: Keselamatan dalam siklus hidup permesinan
1-1
Desain,
Pemilihan material,
Manufaktur,
Assembly,
Transportasi,
Commissioning,
Operasi dan Pemeliharaan
Demolition

## Slide 11
Desain
Material Selection
Manufacturing
Assembly
Transportation
Commissioning
Operation & Maintenance
Demolition

## Slide 12
Conceptual Design
Detailed Engineering
Procurement
Construction
Start-up
High
Low
Ability to Influence Safety
Project Schedule
[Szymberski 1987]
Peran tahapan konstruksi pada aspek keselamatan

## Slide 13
Tingkatan (hierarchy) dalam pengendalian bahaya

## Slide 14: Pengembangan konsep keselamatan konstruksi
Design Kickoff
Design
Internal Review
Issue for Construction
External Review
Trade contractor involvement
Establish design for safety expectations
Include construction and operation perspective
Identify design for safety process and tools
QA/QC
Cross-discipline review
Focused safety review
Owner review

## Slide 15
Safety expectations are addressed in the beginning. There is trade contractor, QA, QC, owner, and contractor involvement throughout the design process. There are multiple reviews and re-designs. This all occurs before the drawings are finally issued for construction.
The key component of this process is the incorporation of site safety knowledge into design decisions. Ideally, site safety would be considered throughout the design process. It is recognized, however, that a limited number of progress reviews for safety may be more practical. The required site safety knowledge can be provided by one or more possible sources of such safety constructability expertise, including trade contractors, an in-house employee, or an outside consultant.

## Slide 28: Pengendalian Risiko secara Teknis (Engineering Controls)
Secara teknis pengendalian keselamatan konstruksi, dapat dilakukan dengan memberikan perhatian khusus pada penggunaan peralatan / kegiatan:
Scaffolds
Fall Protection Anchorages
Hoists
Excavations
Shoring
Lift Slabs

## Slide 29: Recognized Hazards- Fall Hazards
1Photos courtesy of Washington Group International
Unprotected edges
This is an example of a classic fall hazard. The worker is exposed to an unprotected edge. The designer could specify anchorage points in the design so that the worker will have a tie off for fall protection. It should be noted that Designing for Construction Safety is not how or when to use fall protection, it is designing buildings so that either fall protection is not needed, or, installed hardware such as tie-offs.

## Slide 30: Recognized Hazards-Examples Confined Space
Confined spaces are another recognized hazard. Designer can be helpful by designing areas that do not require confined space entry procedures. It should be noted that Design for Construction Safety is how to implement a confined space entry procedure, it is how to design projects so that confined space entry is not required.

## Slide 31: Hidden Hazards-Examples There are many hazards that may be hidden. They are not readily apparent to the worker or the designer.
Underground utilities
Electrical wire buried in a wall
Asbestos
Rot/Decay of structural members
Gas lines
Any hazard uncovered during project execution

## Slide 32: Hidden Hazards-”What If” Analysis
A “What If” analysis is a structured brainstorming methods of uncovering hidden hazards
Select the boundaries of the review and assemble an experienced team
Gather information-video tapes of operation, design documents, maintenance procedures, etc.

## Slide 33: Hidden Hazards-”What If” Analysis “What If” Situation Questions
In a “what if” analysis the design professional or design team needs to brainstorm things that can go wrong (“what if”).
Failure to follow procedures
Procedures are followed, but are incorrect
Equipment failure
Utility failure
Weather
Operator not trained

## Slide 34
Kriteria pengaman permesinan yang ‘baik’ 

## Slide 35
9 POTENSI
BAHAYA MEKANIS
1= terbelit (entanglement)
2= gesekan dan abrasi
3= terpotong (cut)
4= tergunting (shear)
5= tertusuk (stab/puncture)
6= tertumbuk (impact)
7= tergencet (crushing)
8= terjepit kedalam (drawing in)
9= terkena semburan udara bertekanan tinggi, fluida tekanan tinggi, ataupun semburan material padat lain

## Slide 36
Ada 25 ancaman
bahaya bawaan (intrinsik)
dari peralatan mesin

## Slide 37
ancaman
bahaya

## Slide 38
ancaman
bahaya

## Slide 39
ancaman
bahaya

## Slide 40
ancaman
bahaya

## Slide 41
ancaman
bahaya

## Slide 42
ancaman
bahaya

## Slide 43
ancaman
bahaya

## Slide 44
Metode umum pengamanan peralatan mesin 

## Slide 45: Tiga macam pengaman tetap yang umum
Total enclosure fixed guards
Limited access fixed guards
Adjustable access fixed guards

## Slide 46
Total enclosure fixed guards

## Slide 47
Limited access fixed guards

## Slide 48
Limited access fixed guards

## Slide 49
Adjustable access fixed guards

## Slide 50
Adjustable access fixed guards

## Slide 53: Automatic guards/positional guards 

## Slide 54: Beberapa model 
Gates/Fence
Sweep
Mechanical feed
Feed tools
Optical sensors
Ultrasonic
Electric field
Two hands control
Pull-out

## Slide 55
Gates/Fence

## Slide 56
Sweep

## Slide 57
Mechanical feed

## Slide 58
2 hands control

## Slide 59: Interlock guards 

## Slide 60: 2 model rancangan
Control interlock
Scotch interlock

## Slide 61
prinsip interlock

## Slide 62
Control interlock

## Slide 63
Control interlock

## Slide 64
Scotch interlock

## Slide 65: Trip guards 

## Slide 66
Trip guards

## Slide 67
Trip guards

## Slide 68
Trip guards