## Slide 1
13
Bab
Audit Keselamatan
(Safety Audit)

## Slide 2: Safety Audit
Definition
An evaluation to a system damaging or make distruption.
Objective of Safety Audit
to spur companies to systematically identify and rectify weaknesses in their management systems and practices of handling hazardous

## Slide 3: Safety Audit
Systematic and independent by competence personnel
Conducted Periodicly
Methodologies that has been specified
Audit Frequency bases review of audit result previous and danger source evidence
Audit Result is used to process management review

## Slide 4: ELEMENT TO BE AUDITED UNDER THE SAFETY AUDIT
SAFETY POLICY : safe management
SAFETY INFORMATION : safe working procedures and
emergency actions to take in case of emergency.
3. SAFE WORK PRACTICES : safe work procedures have been established to ensure the safe handling, including transportation, loading and unloading, storage and use of hazardous by workers.

## Slide 5: ELEMENT TO BE AUDITED UNDER THE SAFETY AUDIT (Con’t)
MANAGEMENT OF CHANGE: procedures to manage changes to handling of hazardous
5. MAINTENANCE OF FACILITIES : a maintenance system to ensure that all facilities used for the handling hazard
6. GENERAL PLANT INSPECTION/REVIEWS : regular inspections and reviews on handling hazard and procedures for reporting potential hazardous conditions and monitoring the remedial actions established.

## Slide 6: ELEMENT TO BE AUDITED UNDER THE SAFETY AUDIT (Con’t)
TRAINING
Training provided to staff responsible for the handling and storage of hazardous is effective and that such training adequately covers the safety information and safe work practices.
The training shall ensure workers are kept up to date on changes to the types and work procedures in the handling of the hazardous.
8. INCIDENT INVESTIGATIONS
9. EMERGENCY PLANNING AND RESPONSE

## Slide 7: ELEMENT TO BE AUDITED UNDER THE SAFETY AUDIT (Con’t)
HAZARD ANALYSIS.
The company has an established programme to carry out hazard analysis on the handling of hazardous so as to identify, assess and evaluate potential hazards, especially when new hazardous or a significant increase in the quantities of hazardous are handled.
The company has an established procedure to record these hazards and develop and implement means to eliminate the hazards or reduce the hazards to an acceptable level of risk

## Slide 8: ELEMENT TO BE AUDITED UNDER THE SAFETY AUDIT (Con’t)
ADDITIONAL ITEMS
The site shall conforms generally to guidelines pertaining to the safe management of hazardous, i.e. the maintenance of fire alarm and protection systems and other fire safety works conform to the requirements stated in the regulatory requirements

## Slide 9: Incident Investigation
Notes: 1. Reason for picking this topic
2. Discuss proactive strategies vs. reactive strategies
Proactive techniques - conducted to minimize possibility of incidents
Incident investigation and analysis is a reactive technique, conducted to minimize the recurrence of injury
3. Definition of an incident: unplanned action that results in an injury, illness, or property damage
4. Outcomes of an incident
Negative - injury, disease, property damage, litigation costs, lost productivity
Positive - incident investigation, change to eh&s program

## Slide 10: Incidents occur in the presence of hazards
An incident is inevitable if there are no controls in place
It will not always involve personal injury.
An incident may also be property damage, environmental damage or a near miss.

## Slide 11: Purpose of identification
identify any new hazards
identify and choose suitable
controls
Prevent similar accident
recurring in the future
Notes: Ask participants to suggest reasons for conducting an investigation.

## Slide 12: What should be identified?
All incidents that cause
  Injury
  Illness
  Lost time
  Property damage
  All near-miss incidents
Notes: Ask participants to offer suggestions
Several types of incidents:
minor - such as paper cuts to fingers or dropping a box of materials
more serious - someone falling off a ladder or a forklift dropping load
ones that occur over an extended period of time - hearing loss, illness resulting from chemical exposure

## Slide 13: When to identify Incidents?
It is important that any identification occurs as soon as possible.
The less time between an incident and the identification, the more accurate the information that can be obtained.

## Slide 14: How to Conduct an Identification
assumption or judgment →
“must be based on information that is known to be full and accurate”
Notes: I suggest a team approach to an incident investigation.
Certainly the supervisor should be involved in the investigation as he or she is most intimately familiar with the job, tasks, and requirements.
Safety committee representative for the area - has a combination of positive experience - because of his/her knowledge of safety and because of his/her familiarity with the environment
Safety officer - knowledgeable in investigation techniques, good safety practices
Affected employee(s) - they were there when the incident occurred and will know where things went wrong.
Team can be organized for all incidents or scaled down for minor incidents.

## Slide 15: How to Conduct an Identification
Gather information and establish fact:
Who??
What happened??
When did the incident occur??
Where did the incident occur??
Why did the incident occur??

## Slide 16: How to Conduct an Identification
Isolate the contributory factors
This stage is carried out to determine the direct
and underlying causes the incident
Ex. The contributory factors:
Poor vision (incident occurred at dusk)
Trip hazard (uneven path)
Sharp hazard (damaged guard rail)

## Slide 17: How to Conduct an Identification
Determine corrective action
Recommendation must be based on the key contributory factors and the related underlying causes.

## Slide 18: Correct Action
Operator training
Better planning (layout or access)
New equipment/methods

## Slide 19: Emergency planning
Notes: 1. Reason for picking this topic
2. Discuss proactive strategies vs. reactive strategies
Proactive techniques - conducted to minimize possibility of incidents
Incident investigation and analysis is a reactive technique, conducted to minimize the recurrence of injury
3. Definition of an incident: unplanned action that results in an injury, illness, or property damage
4. Outcomes of an incident
Negative - injury, disease, property damage, litigation costs, lost productivity
Positive - incident investigation, change to eh&s program

## Slide 20: Why have an emergency plan??
Emergency planning → an important part
of company operation
Since emergency will occur, preplanning is
necessary to prevent...
Discover unrecognized hazardous
conditions

## Slide 21: OBJECTIVES of THE PLAN
An emergency plan used to specifies
handling to sudden unexpected situation
The objective is to reduce the possible
consequences of the emergency by:
-preventing fatalities and injuries
-reducing damage to building, stock, and
tools

## Slide 22: Why emergency can occur??
Technological:
-Exposure to ionizing radiation,
-building collapse,
-loss of electrical power
Natural Hazard
-tornados
-earthquake

## Slide 23: The possible major impact
Having identified the hazard, the possible major impacts should be considered...
Sequential events (for example, fire after
explosion)
Evacuation
Casualties
Damage to plant infrastructures
Damage to equipment
Loss of vital document

## Slide 24: Organization of emergency plan
One indidual should be appointed and trained to
act as Emergency Co-ordinator
Must be made a particular staff of emergency
plan
External organization that may be avaible to
assist,example:
-fire departement
-ambulances service
-mobile rescue squads
-police departement

## Slide 25: Basic procedures
Identify evacuation routes, alternate means of
escape, make these known to all staff
Specify safe location for staff to gather for
head counts to ensure that everyone has left
the danger zone
Carry out treatment of injured

## Slide 26: Auditing Techniques

## Slide 27: Audit Techniques
Audit Diamond
Ask
Record
Observe
Check
Notes: 11
Notes

## Slide 28: FINDING OUT THE FACTS
Information can be gathered through interviews, observation, checking records and reading documentation.
Records and documentation need to be cross -checked with other records or procedures in that area and in other parts of the system .
You cannot check every record. Take a small sample and check those thoroughly.
Record your checks and observations as you will not be able to remember everything.

## Slide 29: Hazard Spotting
Look for hazardous materials. Check controls
Look at machinery and equipment. Guarding
Check operators. Knowledge and protection.
Look for people exposed to hazards. Access.
Look at handling.
Look for flammable material and ignition sources.
Check methods and control measures.

## Slide 30: Hazard Spotting
Look for distractions.
Look for obstructed walkways, faulty flooring, blind bends and vehicle access.
Look at electrical wiring cables and switches.
Can water contact electrics.
Look for radiation sources. High noise levels.
Vapours, dust and gases near ignition points.
Working up high, or confined spaces.
Food and hygiene practice.

## Slide 31: Initial Review
Where are we now ?

## Slide 32: Review
First stage in developing a system
Identification of Legal Requirements
Identification and evaluation of risks
Identification of issues and liabilities
Evaluation of Policies and Practices
Evaluation of meeting legal requirements

## Slide 33: Review 2
Assessment of previous incidents/accidents
Identification of opportunities
Benefits and liabilities
Analysis of systems in abnormal and emergency conditions
Analysis of Risks
Review of current practices and performance

## Slide 34: Review 3
Review of changes to systems & equipment
Review of current systems
Use of hazardous equipment
Use of hazardous materials
Potential for risk reduction
Current levels of knowledge

## Slide 35: Reporting
Reporting to Top Management to cover
Performance versus the legislative requirements
Gaps in system controls & poor performance
Where controls be tightened and where risks and liabilities can be reduced
Priority areas

## Slide 36: On-Site Auditing

## Slide 37: Audit Team Members
Selected on the basis of team skills
Individuals selected for roles in the audit and availability
Team as a whole must have the technical competences
All team members should be trained in auditing principles and the audit procedures.
Individual auditor requirements depends on the needs of the audit..

## Slide 38: Checklists
Checklists are to help the auditor to remember to cover all the main points
Checklists usually consist of bullet points which the auditor asks questions around
Normally prepared from a process map and added to from the requirements of the legislation.
Useful as a record of the topics covered on the audit as the auditor can put comments against each point

## Slide 39
PROCESS CONTROL MAP
INPUTS
Energy Water
Stacking/Store
Men
Materials Final Product
Methods
Rejects
Machines
Environment
WASTE OUTPUTS
Solids Liquids Emissions Effluent Energy
Packaging Oils Odour Sludge Heat Noise Fire
Materials Solvents Dust Waste Water Light Vibration
Manual/ Mechanical Handling
Fall of objects/persons
Stored Energy Hot /Cold Surfaces
Biological Hazards
Pressurized Vessels
Confined spaces / Drowning
Housekeeping/ Cleanliness
Distractions / Other Persons
Static Electricity & ignition sources

## Slide 40: Typical Checklist Points
Any hazardous materials ?
Electrical devices ? Near Water source ?
Any gases ? Including build up.
Anything pressurised ? Anything hot ?
Machinery and Tools being used.
Anything moving ? People, materials, vehicle
Degree of guarding, containment, protection.
Operator actions – lifting, cutting,

## Slide 41: Typical Checklist Points
Set up activities – Power on/off
Maintenance – regular, irregular
Waste handling, placement
Access – Walkways. Visitors, contractors.
Distractions – Other activities, views
Food and drink.
Ignition sources and flammable materials
Instructions, signs, warnings, labels etc

## Slide 42: Sampling of safety audit

## Slide 43: Preparation
Identify
The location of each active and inactive access point to the facility.
The number, reliability, and security duties of personnel.
Security doors, barriers and lighting.
The location of restricted areas.
The emergency and stand-by equipment available to maintain essential services.

## Slide 44: Identify
The maintenance equipment, storage areas, and flammable materials storage.
Location of escape and evacuation routes and assembly stations.
Existing security and safety equipment for protection of personnel and visitors.
Response procedures for fire or other emergency conditions.
Procedures for monitoring site and perimeter, personnel, vendors, etc…

## Slide 45: Identify
Existing contracts with private security agencies.
Procedures for controlling keys and other access prevention systems.
Procedures for vehicle access, deliveries and stores operations.
Response capability to security incidents.
Previous reports on security needs.
Any other existing security procedures, systems, equipment, or personnel.

## Slide 46: Report
Summary of how the assessment was conducted.
A description of existing security measures, including inspection, control and monitoring equipment, personnel, etc…
A description of security measures that could be used to address each vulnerability.
A list of the key site assets and operations that are important to protect.

## Slide 47: Report
A list of identified weaknesses, including human factors, in the infrastructure, policies, and procedures of the site.
Elements of the site:
Physical security
Structural integrity
Personnel protection systems
Procedural policies
Telecommunication systems and computer systems
Relevant transportation infrastructure
Utilities

## Slide 48: Report
Is confidential.
Should be factual.
Should be presented to Top Management.
Should result in Commitment and Actions
A Site Security Policy Developed.
A Security Management Representative.
A Site Security Plan